## Slide 1: Robust Physical-World Attacks on Deep Learning Visual Classification
Dat Quoc Ngo
University of Texas at Dallas
September 24, 2021

## Slide 2: Agenda
Background
  Deep Learning in Computer Vision
  Safety Concern
Challenges
Related Work
Solution
Experiments & Evaluation

## Slide 3: Background: DL in Computer Vision
Deep Neural Networks (DNNs) achieved state-of-the-art results in many Computer Vision tasks
e.g. YOLOvx for Object Detection
Applied in physical systems: UAVs, robots

## Slide 4: Background: Safety Concern
Concern of DNNs’ vulnerability to adversarial perturbations (aka digitally and physically modified visual input)
=> Misbehavior of systems in potentially dangerous ways
=> Raising safety transportation concerns

## Slide 5: Background: Road Sign Classification
Significant in self-driving systems and transportation
Challenging to hide perturbations due to simplicity
Notes: Image Reference: Wu et al.

## Slide 6: Challenges
Environment Conditions:
  Continuous change of distance and angle of a camera
  Lightning/weather conditions, and debris on camera
Spatial Constraints:
  Background of road signs changes
  Difficult to place adversarial examples on road signs

## Slide 7: Challenges (continued)
Imperceptibility Limits
  Tiny modifications are imperceptible
Fabrication Error
  All modification must be realistic (i.e. colors)
Dependent on sensing hardware
Notes: Image Reference: Eykholt et al.

## Slide 8: Related Work
Digital Adversarial Examples
Full-access to classifiers
Reverse engineering to
  Extract models
  Generate adversarial examples to fool classifiers
  e.g. GAN
Notes: Reference: Research Gate(https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.researchgate.net%2Ffigure%2FThe-original-generative-adversarial-network-GAN-model-In-simple-terms-G-wants-to_fig1_340481789&psig=AOvVaw0kUBHbYUu5UApI1lV0TD1X&ust=1632605270565000&source=images&cd=vfe&ved=0CAwQjhxqFwoTCJDt3dzGmPMCFQAAAAAdAAAAABAY)

## Slide 9: Related Work (continued)
Physical Adversarial Examples
Not modify objects, print digitally perturbed masks on objects
Change physical conditions
e.g. post, distance/angle from camera
Notes: Image Reference: Eykholt et al.

## Slide 10: Notation
x - original clean image
x’ - adversarial image that is closely similar to x
f(.) - road sign classifier
y - ground truth
y* - targeted class

## Slide 11: Solution & Evaluation
Robust Physical Perturbations (RP^2)
Focus on road sign classification
Generate adversarial examples in various physical conditions
Two-stage evaluation: in lab and in field tests

## Slide 13: Position of masks
Target weak areas of road signs
Pipeline:
  L1 to compute perturbations - location of weak areas
  L2 to recompute perturbations

## Slide 14: Loss Function
||𝛿|| - Euclidean Distance between x and x’
J - cross entropy

## Slide 15
Considering Fabrication Error & Alignment
NPS - printer color reproduction errors
T(.) - alignment function

## Slide 16: Testing Environments
Stationary Tests:
  Clean images C taken at fixed positions
  With varying distances D and angles G
  Adversarial images A(c^dg)
Drive-by Tests
  Camera on moving platforms
  Driving speed: 0-20 mph

## Slide 17: Experiments
Classifiers:
  LISA-CNN (pretrained w/ U.S. traffic signs)
  GTSRB-CNN (pretrained w/ German traffic signs)
Datasets:
  LISA: 47 road signs but only 17 common signs in use
  Own dataset: 181 stop sign images

## Slide 18: Evaluation: Success Attack Rate

## Slide 19: Slide Title